Spectre RT3G router and Wzzard Edge Node device

Use the Spectre router and Wzzard device(s) to connect to the IBM Internet of Things Cloud. Then, you can visualise the data generated by any Wzzard connected sensors on the Quickstart page. This demo uses a thermocoil sensor attached to a Wzzard Edge Node to generate the temperature data to be sent to the cloud.

Ingredients
Hardware Requirements

- Spectre RT3G router
- Wzzard Edge Node device (with power supply or batteries)
- Thermocoil to attach to Wzzard Edge Node device

Prepare
Get your device ready
- Connect the Spectre router to the internet (can use ethernet connection or cellular network).
- Power up the Wzzard Edge Node device and attach the thermocoil to the I/O.
- Log into the router over ssh (ssh root@rooter_ip)

Connect (QuickStart)
Internet of Things Cloud QuickStart connection
Download the demo module from GitHub:
wget https://github.com/bb-elec/iot-SpectreWzzard/archive/master.zip
 unzip master.zip
 cd iot-SpectreWzzard-master

Run the install script:
 ./install.sh

This process adds the required modules and libraries to the router and runs them. To check that the service is running, run the following commands:
 cd /opt/IBM_Message_Router/etc
 ./init status

If the process is stopped (didn't start correctly), run the following command to restart it:
./init restart
The ./init status command should now tell you the module is running.

Visualise
Real-time visualisation of device data.

- Find the MAC address of the Spectre router by running the getdeviceid script in the repository you downloaded at the start (iot-SpectreWzzard repository).
  ./getdeviceid.sh
- Enter your MAC address here.